## Slide 1
This ground is reserved capacity. A data center pours the option in concrete.
1958
Fifth runway enters
Dulles designs
1985
Capacity carried in
the master plan
2005
FAA approves fourth
and fifth runways
2024
27.25M passengers;
United ≈70% of flights
2025
Board reaffirms path
toward ≈90M passengers
The parcel sits inside the RWY 1L approach and RWY 19R departure surfaces of a growing airfield.
Sources: MWAA master-plan update (2025); FAA Record of Decision (2005); FFXnow passenger record; Simple Flying market-share analysis.
Notes: Lead with irreversibility, not the hazard list. Each hazard can be evaluated and conditioned. The permanent commitment of reserved capacity land cannot. Avoid claiming that the parcel lies on the published fifth-runway alignment; the relevant claim is the 1L/19R protected surfaces and extension capacity.
[Sources]
- https://www.mwaa.com/news/dulles-master-plan-update-sets-framework-decades-airport-development
- https://www.ffxnow.com/2025/07/17/new-master-plan-for-dulles-airport-envisions-growth-to-90-million-annual-passengers/
- https://www.flydulles.com/d2-projects-future-fifth-runway
[/Sources]

## Slide 2
The law leaves 25 to 200 feet of air above this parcel.
RWY END
1,000 ft
2,000 ft
3,000 ft
4,000 ft
0–250 FT AGL
50:1 APPROACH
40:1 DEPARTURE
3° GLIDEPATH
50-FT
HALL
≈102 ft
≈155 ft
≈207 ft
ALSF-2 · 2,400 FT
50-ft object meets 50:1 surface at ≈2,500 ft
25 ft allowable at 1,000 ft on the 40:1 surface
WILDLIFE SEPARATION / 10,000 FT
pond
FAA HEIGHT / 1–4K FT
Chart: 
| 1 | 2 | 3 | 4
50:1 approach | 20 | 40 | 60 | 80
40:1 departure | 25 | 50 | 75 | 100
Notes: flat terrain at runway-end elevation; generic massing; published FAA geometry, not the unpublished site plan.
Sources: 14 CFR 77.19; FAA AC 150/5300-13B; FAA ALSF-2 specifications; FAA AC 150/5200-33C; analyst geometry.
Notes: This is the mechanism slide. The correct claim is the geometry, not a proven upset. The published surfaces leave little vertical margin for a generic 50-foot hall and rooftop plant. FAA plume guidance rates overall disruption risk low for transport-category jets; do not claim that plume will endanger heavy aircraft.
[Sources]
- https://www.ecfr.gov/current/title-14/chapter-I/subchapter-E/part-77/subpart-C/section-77.19
- https://www.faa.gov/airports/resources/advisory_circulars/
- https://www.faa.gov/about/office_org/headquarters_offices/ato/service_units/techops/navservices/lsg/als
- https://www.faa.gov/documentLibrary/media/Advisory_Circular/150-5200-33C.pdf
[/Sources]

## Slide 3
The 2018 sale protected capacity first. This proposal reverses the order.
THE COUNTER-CASE, AT FULL STRENGTH
$236.5M
424 acres · ≈$558K per acre
≈70%
Estimated global internet traffic through Ashburn
GA 24
Airport should be self-sustaining
LOW
FAA overall plume disruption risk
THE ANSWER, FROM THE SAME RECORD
2018 DISCIPLINE
Build runway +
support area
Sell remaining
surplus
CURRENT PROPOSAL
Sell reserved
capacity
Foreclose the
1L/19R option
Condition every hazard. You still cannot reverse a land commitment.
Sources: MWAA Western Lands sale; Lightyear Data Center Alley guide; FAA Grant Assurance 24; FAA thermal-plume guidance.
Notes: Do not caricature the opposition. Concede the verified revenue, connectivity, self-sustainability, and plume points. Then use the 2018 sale as the governing rule: MWAA protected capacity first and sold only the surplus remaining after the fourth runway and support area were built.
[Sources]
- https://www.mwaa.com/news/airports-authority-announces-sale-424-acres-western-lands-dulles-international
- https://lightyear.ai/blogs/ashburn-colocation-data-center-alley
- https://www.faa.gov/airports/aip/grant_assurances/assurances-airport-sponsors-2025
- https://www.faa.gov/sites/faa.gov/files/airports/environmental/land_use/Technical-Guidance-Assessment-Tool-Thermal-Exhaust-Plume-Impact.pdf
[/Sources]

## Slide 4
The ask: the gate, not a slogan — sell the surplus, keep the runway.
1
NO APPROVAL
Do not approve from a circulated project email.
→
2
FAA REVIEW
ADO coordination + Form 7460-1 evaluation.
→
3
TECHNICAL PROOF
Glare, plume, EMI + wildlife-safe stormwater.
→
4
FORMAL PLAN
ALP amendment consistent with the master plan.
→
5
REJECT THIS SITE
No study cures foreclosure of reserved capacity.
ARGUE ON THE FAA'S OWN STANDARD
SECTION 163 · CONFIRM WITH COUNSEL
A
Materially affects safe, efficient aircraft operation
B
Endangers people or property on the ground
C
Diminishes prior federal investment
≈$64M in two 2026 grants
Grant Assurances 19–22 and 29 bind MWAA. The federal lease runs to 2100.
Sources: 14 CFR Part 77; FAA Sponsor Assurances; 49 U.S.C. 47107; Section 163; FY2026 grants; MWAA federal lease.
Notes: The recommendation is a gate and a siting decision. Require every FAA study and formal plan action, then reject this location because no favorable study can cure the irreversible commitment of reserved capacity. Section 163 was revised in 2024; counsel should confirm the current framework before a formal submission.
[Sources]
- https://www.ecfr.gov/current/title-14/chapter-I/subchapter-E/part-77
- https://www.faa.gov/sites/faa.gov/files/airports/aip/grant_assurances/airport-sponsor-assurances-aip.pdf
- https://www.federalregister.gov/documents/2023/12/08/2023-27017/policy-regarding-processing-land-use-changes-on-federally-acquired-or-federally-conveyed-airport
- https://www.ffxnow.com/2026/05/20/dulles-airport-lands-41m-federal-grant-for-concourse-e-construction/
- https://www.mwaa.com/news/secretary-transportation-and-airports-authority-sign-lease-extension-operation-washingtons
[/Sources]