## Slide 1
Do not build a data center inside the approach surfaces of a Cat II/III ILS runway.
Proposed data center
RWY 1L / 19R
RWY 1L approach / RWY 19R departure surfaces
ALSF-2 approach lights
9,400-ft Cat II/III ILS runway with ALSF-2 approach lighting.
Schematic, not to scale. Source: FAA instrument approach data, KIAD RWY 01L/19R — Cat II/III ILS, ALSF-2 (FlightAware approach plate).
Notes: Open with the claim, not background. The site sits inside the RWY 1L approach and RWY 19R departure surfaces of IAD's Cat II/III ILS runway — the most instrument-critical corridor on the airfield. This is strategic capacity land; the recommendation is do not proceed at this location, not do not proceed with the developer.

## Slide 2
A data center puts three interference vectors under one glide path.
Cat II/III glide path
Data center
1
2
3
1
Plume turbulence to 1,000 ft above the tower (AIM § 7-6-16)
2
Open-water basin draws wildlife (AC 150/5200-33C)
3
Metallic mass and emissions degrade the ILS signal (Order 6750.16E)
“Placing an object outside the critical area does not guarantee non-interference with the ILS signal in space.” — FAA Order 6750.16E
Schematic, not to scale. Sources: FAA AIM § 7-6-16 (Change 3, Sept. 5, 2024); FAA AC 150/5200-33C; FAA Order 6750.16E (Apr. 10, 2014).
Notes: This is the whole mechanism in one picture. The hazards are physical, not procedural: turbulence a pilot cannot see, wildlife the corridor cannot tolerate, and signal interference no lease term can waive. FAA Technical Operations certifies the ILS and is not a party to any lease.

## Slide 3
The FAA has already called this hazard class incompatible — and it holds the enforcement pen.
PRECEDENT
Thermal plumes “incompatible with airport operations” — FAA guidance, 2015
Cooling-tower plumes a hazard to Long Beach departures — Puente docket
ENFORCEMENT
Section 743 preserves FAA review: aircraft safety, ground safety, federal investment
Grant Assurances 19, 20, 29 attach independently
14 CFR Part 16: penalties up to 3x diverted revenue
Sources: FAA Technical Guidance Memorandum, Sept. 24, 2015; CEC Docket 15-AFC-01; FAA Reauthorization Act of 2024 § 743; FAA Airport Sponsor Assurances, Apr. 2025; 14 CFR Part 16; 49 U.S.C. § 46301(a)(3).
Notes: This is precedent, not prediction. The FAA classified thermal plumes as incompatible with airport operations in 2015 and applied that finding against a power plant near Long Beach Airport. Section 743 preserves FAA jurisdiction on exactly the safety and federal-investment grounds this project implicates, and Assurances 19, 20, and 29 each attach independently.

## Slide 4
MWAA's own data-center precedent argues for a different parcel, not this one.
2018 Western Lands
424 acres to Digital Realty
Outside the approach surfaces
ALP change subject to NEPA
Proposed site
Inside the 1L approach and 19R departure surfaces
No FAA coordination to date
Not on the approved ALP
Section 743 preserves FAA review on safety and federal investment — assume review; do not lean on the 45-day window.
Sources: MWAA Western Lands release, 2018; FAA Reauthorization Act of 2024 § 743; FAA ALP Preliminary Instructions Memorandum, Oct. 3, 2024.
Notes: Take the objection at full strength: data centers can work at IAD — MWAA proved it in 2018. But the Western Lands deal sat outside the protected surfaces and went through FAA process. The precedent validates the use and condemns the site. No documented incident in Loudoun County's roughly 26M sq ft of data centers, but none of them sit inside an ILS approach corridor; absence of an accident is not permission.

## Slide 5
Halt, file the 7460-1, and move the deal — the aeronautical study governs, not the lease.
1
Halt advancement pending FAA coordination
PLANNING
2
File Form 7460-1; require a No Hazard determination
PLANNING
3
Move the deal to master-plan non-aeronautical zones
COMMERCIAL REAL ESTATE
4
Route Grant Assurance exposure; ALP re-enters the master plan
GENERAL COUNSEL
Sources: FAA OE/AAA process, 14 CFR Part 77 and Form 7460-1; FAA ALP SOP 2.00; FAA Airport Sponsor Assurances, Apr. 2025.
Notes: Close on the decision anchor: the governing event is the Form 7460-1 filing and the aeronautical study that follows — every commitment made before that study returns is made against an undefined regulatory outcome. This redirects the deal, not the developer. The ask is a halt-and-resite, not a kill.